CELT Technical Note 4

Requirements for CELT Bearings, Drives, Encoders

Jerry Nelson

21 March 2001

Definitions

Telescope is an altitude-azimuth system

The component that moves in altitude or elevation is called the “tube.”

The component that moves in azimuth is called the “yoke.”

Coordinates:

Origin of coordinate system is at the intersection

of the elevation, azimuth and optical axes

Tube:

+z is along the optical axis, looking out to the stars,

+x is along axis of rotation (elevation axis)

+y is orthogonal, in a right handed coordinate system, and points downwards

when the telescope is pointing towards the horizon

Yoke

+z is vertical

+x is same as for the tube

+y is the orthogonal coordinate in a right handed system

All numbers are tentative

Mass and Moment of Inertia

Tube:

M = 4.17e5 kg

Ix = 7.795e7 kg-m2

Iy = 7.803e7 kg-m2

Iz = 4.856e7 kg-m2

Yoke:

M = 4e5 kg

Ix = 4e7 kg-m2

Iy = 9e7 kg-m2

Iz = 9e7 kg-m2

Motion Requirements

Pointing		within 1 arcsecond rms over all sky

Tracking (open loop)	0.02 arcsecond rms in 10 s

0.1 arcsecond rms in 10 minutes

0.5 arcsecond rms in 1 hr

Guiding (closed loop, AO off)	within 0.02 arcsecond rms over 10 min.

Within 0.05 arcsecond rms over 1 hr

Focus 			within 0.02 arcsecond (80%)

Slewing		360° azimuth, 65° elevation in 5 minutes

1 arcsecond on sky	1 s

10 arcsecond on sky	3 s

100 arcsecond on sky	10 s

1000 arcsecond on sky	30 s

slewing goals are 50% of above values

Sky coverage	Unvignetted above 25°

<2° zenith blind spot diameter

Observing range

Azimuth	100.5° ±220.5°

Elevation	25°-89°